OPERATIONAL GUIDELINE

94-05-08-03

Date:		8 May 1994

Subject:	Role of the Crash Truck Driver

Upon arrival at the scene of a crash truck call, the driver of the crash truck shall assume the role of Engineer/Operator, and shall do the following:

Park the truck tactically, set the brake, and set the fast idle.

Set the wheel chocks.

For operations conducted from the truck (primarily involving the use of the hydraulic rescue system):

Make sure the main generator is started and appropriate scene lights are switched on.

Make sure the electric hydraulic pumps are started.

Stay with the truck and control the dump valves.

For operations conducted away from the truck:

Help move equipment to the equipment staging area, as required.

Help rig hydraulic, electric, pneumatic, and mechanical systems as required.

Assume control of switches, valves, and levers once systems are rigged.

APPROVED:

___________________________________________________	_____________________________

Alan Walters, Squad Truck Team Supervisor, Rescue 9	Date

___________________________________________________	_____________________________

Capt. John Fusco, Squad Commander, Rescue 9	Date